## Slide 1: Status of the LHC: Past, Present and Future
24th Rencontres de Blois
May 27, 2012
Sergio Bertolucci
CERN
LHC

## Slide 2
S. Myers QUB March 11, 2009
2
The LHC
Notes: 2

## Slide 4: LHC: Some of the Technical Challenges
Circumference (km) | 26.7 | 100-150m underground
Number of Dipoles | 1232 | Cable Nb-Ti, cold mass 37million kg
Length of Dipole (m) | 14.3 | 
Dipole Field Strength (Tesla) | 8.4 | Results from the high beam energy needed
Operating Temperature (K) | 1.9 | Superconducting magnets needed for the high magnetic field Super-fluid helium
Current in dipole sc coils (A) | 13000 | Results from the high magnetic field 1ppm resolution
Beam Intensity (A) | 0.5 | 2.2.10-6 loss causes quench
Beam Stored Energy (MJoules) | 362 | Results from high beam energy and high beam current 1MJ melts 2kg Cu
Magnet Stored Energy (MJoules)/octant | 1100 | Results from the high magnetic field
Sector Powering Circuit | 8 | 1612 different electrical circuits

## Slide 5: The LHC Timeline
?, IR
4x
, bunch spacing 25 ns
~20-25 fb-1
~75-100 fb-1
~350 fb-1
, bunch spacing 25 ns
, bunch spacing 50 ns
Go to design energy, nominal luminosity
Injector and LHC Phase-1 upgrade to ultimate design luminosity
HL-LHC Phase-2 upgrade, IR, crab cavities?
√s=14 TeV, L=5x1034 cm-2 s-1, luminosity levelling
√s=14 TeV, L~2x1034 cm-2 s-1, bunch spacing 25 ns
√s=13~14 TeV, L~1x1034 cm-2 s-1, bunch spacing 25 ns
√s=7~8 TeV, L=6x1033 cm-2 s-1, bunch spacing 50 ns
LHC startup, √s = 900 GeV

## Slide 6: LHC: First collisions at 7 TeV on 30 March 2010
CMS
ALICE
LHCb
Peak Luminosity for First Run 1027 cm-2 s-1

## Slide 7: Maximizing the Luminosity

## Slide 8: Peak Luminosity 2010
2010 Goal
Update needed
Goal for 2010 : 1E32
Peak Luminosity 2.2E32

## Slide 9
Integrated Luminosity in 2010
45pb-1 recorded

## Slide 11: 2011 Operation (Goal for the year was 1000 pb-1, i.e 22 times more than 2010)

## Slide 12: “Lumi leveling” first tested 15th April 2011

## Slide 13: Luminosity Leveling via beam Separation
Introduced luminosity leveling for LHCb  can run at optimal μ and Lmax
Since end of May running at constant L ~ 3-3.5∙1032 cm-2s-1 with μ ~ 1.5
LHCb want maximum time in physics and not an increase in peak performance

## Slide 14: History of 2011 Peak Luminosity
Chart: Peak Luminosity / 10+30 cm-2 s-1
MD, technical stop
MD, technical stop
Mini-Chamonix
Intermediate energy run, technical stop, scrubbing
75 ns
50 ns
Emittance
Reduction and intensity increase
MD, technical stop
b* = 1m
Intensity Ramp Up
b* = 1.5m

## Slide 15
Goal 2011
Protons
~ 6000 pb-1

## Slide 16
Heavy Ion Operation

## Slide 17: A word from our suppliers

## Slide 18
In 2010:
Peak ~18E24; Integrated ~18ub-1 Max 137 bunches, larger *, smaller bunch intensities
2010
2010
Peak and Integrated luminosity
356 bunches

## Slide 19: Running in 2012: boundary conditions
The LHC machine must produce enough integrated luminosity to allow ATLAS and CMS to independently discover/exclude the Higgs before the start of LS1.
We must also prepare for the proton-lead ion run at the end of the year.
We must (in 2012) do the necessary machine experiments to allow high energy, useful high luminosity running after LS1.
Pile up and 25ns

## Slide 20
Integrated luminosity needed for Discovery of Higgs

## Slide 21
40 reconstructed vertices
High PU run October 25, 2011

## Slide 22
Huge efforts over last months to prepare for high lumi and pile-up expected in 2012:
optimized trigger and offline algorithms (tracking, calo noise treatment, physics objects)
 mitigate impact of pile-up on CPU, rates, efficiency, identification, resolution
in spite of x2 larger CPU/event and event size  we do not request additional computing
resources (optimized computing model, increased fraction of fast simulation, etc.)
The challenge:
Z μμ
Z μμ event from 2012 data with 25 reconstructed vertices
2011: average 12, with tails up to ~20 comparable to what expected at design luminosity
(due to: 50 ns operation; several machine parameters pushed beyond design, etc.)
2012: higher energy, more squeezed beams (β*=0.6m)  already experienced an average
of ~25 events/xing at the beginning of the fill with tails up to ~30.
PILE-UP = number of interactions per crossing

## Slide 23: Reminder 2012 run configuration
Energy – 4 TeV
Bunch spacing - 50 ns
Collimator settings – tight
Atlas and CMS beta* - 60 cm
Alice and LHCb beta* - 3 m
  Natural satellites versus main bunches in Alice
Real Challenge
2 high luminosity experiments(ATLAS, CMS)
1 mid-luminosity (LHCb) x20 lower
1 low-luminosity (ALICE) x10,000
Also TOTEM and ALFA

## Slide 24: Estimated Peak Luminosity with 50ns (2012)
Estimated Peak Luminosity of 5.8x1033

## Slide 25
First (most critical) Break-point
Second Break-point
Check if we are on track to produce sufficient integrated luminosity for the Higgs
If needed we can delay the start of LS1 by up to 2 months

## Slide 26: Peak Luminosity (as of today)
Estimated for 2012

## Slide 27: Luminosity Evolution (as of today)


## Slide 28: LS1: towards operation at ~ 7TeV/beam
LS1 Work
  Repair all the defective interconnects
  Consolidate all interconnects with new design
  Finish off pressure release valves (DN200)
  Bring all necessary equipment up to the level needed for 7TeV/beam

## Slide 29: LHC MB circuit splice consolidation proposal
Phase I
Surfacing of bus bar and installation of redundant shunts by soldering
Phase II
Application of clamp and reinforcement of nearby bus bar insulation
Phase III
Insulation between bus bar and to ground, Lorentz force clamping

## Slide 30
…then operation at 6.5TeV per beam
Assumptions
E=6.5TeV
β* = 0.5m
All other conditions as in 2012 i.e. no improvement (yet) in injector brightness, LHC availability same etc

## Slide 31: 6.5TeV: 25ns
6.5Tev: 25 ns
β* = 0.5m
148 days of physics
Lpeak ~7.5E33 µ = ~17
Days since start of 2015 run

## Slide 32: 6.5TeV per beam with 50ns
6.5Tev: 50 ns
β* = 0.5m
148 days of physics
Lpeak ~10.5E33 µ = ~50
Days since start of 2015 run

## Slide 33: The LHC Timeline
?, IR
4x
, bunch spacing 25 ns
~20-25 fb-1
~75-100 fb-1
~350 fb-1
, bunch spacing 25 ns
, bunch spacing 50 ns
Go to design energy, nominal luminosity
Injector and LHC Phase-1 upgrade to ultimate design luminosity
HL-LHC Phase-2 upgrade, IR, crab cavities?
√s=14 TeV, L=5x1034 cm-2 s-1, luminosity levelling
√s=14 TeV, L~2x1034 cm-2 s-1, bunch spacing 25 ns
√s=13~14 TeV, L~1x1034 cm-2 s-1, bunch spacing 25 ns
√s=7~8 TeV, L=6x1033 cm-2 s-1, bunch spacing 50 ns
LHC startup, √s = 900 GeV

## Slide 34: LS2 : 2018, LHC Injector Upgrades
Connect Linac4 to PS Booster, (if not already achieved)
  New PS Booster injection channel
Upgrade PS Booster from 1.4 to 2.0 GeV
  New Power Supplies, RF system etc.
  Upgrade transfer lines, instrumentation etc.
Upgrades to the PS
  New Injection region for 2.0 GeV Injection
  New/Upgraded RF systems
  Upgrades to Feedbacks/Instrumentation etc.
Upgrades to the SPS
  Electron Cloud mitigation – strong feedback system, or coating of the vacuum system
  Impedance reduction, improved feedbacks
  Large-scale modification to the main RF system

## Slide 35: The ultimate LHC: HL-LHC Specifications
35
Integrated luminosity: 200 fb-1 to 300 fb-1 per year
Leveled peak luminosity: L = 5 1034 cm-2 sec-1
Oliver Brüning BE-ABP
Total integrated luminosity: ca. 3000 fb-1
Virtual peak luminosity: L > 10 1034 cm-2 sec-1
Chamonix, 9 February 2012

## Slide 36: HL-LHC Performance Estimates
36
Parameter | nominal | 25ns | 50ns
N | 1.15E+11 | 2.0E+11 | 3.3E+11
nb | 2808 | 2808 | 1404
beam current [A] | 0.58 | 1.02 | 0.84
x-ing angle [mrad] | 300 | 475 | 520
beam separation [s] | 10 | 10 | 10
b* [m] | 0.55 | 0.15 | 0.15
en [mm] | 3.75 | 2.5 | 3.0
eL [eVs] | 2.51 | 2.5 | 2.5
energy spread | 1.00E-04 | 1.00E-04 | 1.00E-04
bunch length [m] | 7.50E-02 | 7.50E-02 | 7.50E-02
IBS horizontal [h] | 80 -> 106 | 25 | 17
IBS longitudinal [h] | 61 -> 60 | 21 | 16
Piwinski parameter | 0.68 | 2.5 | 2.5
geom. reduction | 0.83 | 0.37 | 0.37
beam-beam / IP | 3.10E-03 | 3.9E-03 | 5.0E-03
Peak Luminosity | 1 1034 | 7.4 1034 | 8.4 1034
minimum b*
(Leveled to 5 1034 cm-2 s-1)
nominal bunch length and minimum b*: ‘HL-LHC Kickoff+’
Events / crossing | 19 | 141 | 257 | 95 | 190
Oliver Brüning BE-ABP
5.6 1014 and 4.6 1014
p/beam
sufficient room for leveling
(with Crab Cavities)
Virtual luminosity (25ns) of
L = 7.4 / 0.37 1034 cm-2 s-1
= 20 1034 cm-2 s-1 (‘k’ = 4)
Virtual luminosity (25ns) of
L = 8.4 / 0.37 1034 cm-2 s-1
= 22.7 1034 cm-2 s-1 (‘k’ = 4.5)
Chamonix, 9 February 2012
Notes: 50ns beam option provides HL-LHC performance levels at ultimate total beam currents; only the ‘large beta*’ option reaches beam-beam limit; IBS growth rates are a concern!; low beta option has 50% higher performance potential

## Slide 37: R&D Superconducting Links
Motivated by the need to remove the power converters out of the tunnel, avoiding radiation effects
Φ = 62 mm
7 × 14 kA, 7 × 3 kA and 8 × 0.6 kA cables – Itot120 kA @ 30 K
MgB2 (or other HTS)
Also DFs with current leads removed to surface Definitive solution to R2E problem
Make room for shielding unmovable electronics
Make much easier maintnance and application ALARA

## Slide 38: Preliminary HE-LHC - parameters
Not only luminosity: High Energy LHC
Very preliminary with large error bars

## Slide 39: HE-LHC – LHC modifications
2-GeV Booster
Linac4
SPS+,
1.3 TeV, 2030-33
HE-LHC
2030-33

## Slide 40: HE-LHC – main issues and R&D
High-field 20T dipole magnets based on Nb3Sn, Nb3Al, and HTS
High-gradient quadrupole magnets for arc and IR
Fast cycling SC magnets for ~1.3TeV injector
Emittance control in regime of strong SR damping and IBS
Cryogenic handling of SR heat load (first analysis; looks manageable)
Dynamic vacuum

## Slide 41: Summary
The First two years of LHC operation have produced sensational performance: well beyond our wildest expectations
The combination of the performance of the LHC machine, the detectors and the Grid have proven to be a terrific success story in particle physics.
However, we must remain extremely vigilant with respect to the protection of the machine (120MJ of stored energy) and hope that there are no old “unexploded bombs” in the hardware!!
In the absence of any major technical failure, the LHC machine WILL produce enough integrated luminosity in 2012 to allow the detectors to discover or exclude the Higgs Boson.
The high energy operation after the Long Shutdown will be another exciting era in discovery physics

## Slide 42
Thank you!